## Slide 1: Smart CommunicationPlatformsfor Smart Cities - Evolution from Next Generation Network towards Future Internet
Prof. Dr. Thomas Magedanz,
FOKUS Next Generation Network Infrastructures (NGNI)
{thomas.magedanz, niklas.blum}@fokus.fraunhofer.de
TU Berlin Chair for Next Generation Networks (AV)
thomas.magedanz@tu-berlin.de

## Slide 2: Evolution of Telecommunication Platforms toward Smart Communications
Mobile Broadband
IP Networks
Evolved Packet
Core (EPC)
Open APIs
OSA/Parlay/JAIN
Intelligent
Network (IN)
IP Multimedia
System (IMS)
Telecom APIs
Parlay X, GSM One,
OMA NGSI, etc
Cloud Applications:
RCS, UC, eGov, eHealth,
eTransport, eUtilities
IN Overlay
Architecture
Circuit Switched
Networks
IT Impact on Telecoms
PSTN
GSM
IP
Service Delivery Platform
(SOA based)
IP Networks
(NGN)
DSL
UMTS
WLAN
Cable
Network Abstraction
Open Service APIs (Enablers)
VoIP / SIP
LTE
WiMAX
WLAN
All-IP
Smart City /
Future Internet
Core Platform
APIs (Enablers)
Network Abstraction
IN Services
based on SIBs
IMS
MTC

## Slide 3: Evolution of Telecommunication Platforms toward Smart Communications
Mobile Broadband
IP Networks
Evolved Packet
Core (EPC)
Open APIs
OSA/Parlay/JAIN
Intelligent
Network (IN)
IP Multimedia
System (IMS)
Telecom APIs
Parlay X, GSM One,
OMA NGSI, etc
Cloud Applications:
RCS, UC, eGov, eHealth,
eTransport, eUtilities
IN Overlay
Architecture
Circuit Switched
Networks
IT Impact on Telecoms
PSTN
GSM
IP
Service Delivery Platform
(SOA based)
IP Networks
(NGN)
DSL
UMTS
WLAN
Cable
Network Abstraction
Open Service APIs (Enablers)
VoIP / SIP
LTE
WiMAX
WLAN
All-IP
Smart City /
Future Internet
Core Platform
APIs (Enablers)
Network Abstraction
IN Services
based on SIBs
IMS
MTC
Internet of Things
Internet of Services
Network of the Future
Future Internet Research

## Slide 4: Related FOKUS Testbed Evolution
Open APIs
OSA/Parlay/JAIN
Intelligent
Network (IN)
IP Multimedia
System (IMS)
Telecom APIs
Parlay X, GSM One,
OMA NGSI, etc
FI Applications
Smart Cities, eGov, eHealth,
eTransport, eUtilities
IN Services
based on SIBs
IN Overlay
Architecture
Circuit Switched
Networks
IT Impact on Telecoms
PSTN
GSM
IP
Service Delivery Platform
(SOA based)
IP Networks
(NGN)
DSL
UMTS
WLAN
Cable
Network Abstraction
Open Service APIs (Enablers)
VoIP / SIP
Mobile Broadband
IP Networks
LTE
WiMAX
WLAN
Evolved Packet
Core (EPC)
All-IP
Future Internet
Core Platform
APIs (Enablers)
Network Abstraction
OSA/Parlay
Playground
Future Internet Research

## Slide 5
OSA/Parlay
Playground
Related FOKUS Testbed Evolution

## Slide 6: Fraunhofer Testbeds / Playgrounds Evolution
www.FUSECO-Playground.org
www.SC-Playground.org
NGN2FI Lab
G-Lab Deep, Panlab, Openlab

## Slide 7: Fraunhofer Testbeds / Playgrounds Evolution
www.FUSECO-Playground.org
www.SC-Playground.org
Internet of Things
Internet of Services
Network of the Future

## Slide 8
www.FUSECO-Playground.org
www.SC-Playground.org

## Slide 9: Future Internet … to make our cities smart A Smart City is a huge Future Internet Show Case
E-Health
Education
Security
Energy
Communications
Mobility
E-Living
Culture
Urban
Production
Signal Transmission & Networks
Transport &
Traffic
Politics &
E-Government
www.fokus.fraunhofer.de/go/ngn2fi

## Slide 10: Assessment of Platform Requirements
Separation of communication-centric services and enablers into three categories:
  Machine-to-Machine (M2M) Communication
  Human-to-Human (H2H) Communication
  Overarching Services and Enablers
Mapping of service and enablers towards different service domains where applicable
Exemplary refinement for one specific service vertical (facility management)

## Slide 11: Ubiquitous Communication Enablers & Sectors
Enabling Services |  | Business / Collaboration | Leisure time communication | E-Health | Utilities | Facility Management | E-Energy | Logistics
Machine-2-machine | Retrieve data |  |  | X | X | X | X | X
 | Control devices |  |  | X | X | X | X | X
 | Send data |  |  | X | X | X | X | X
Human-2-human | A/V Call | X | X | X | X | X |  | 
 | A/V conference | X |  | X | X | X |  | 
 | Messaging / File transfer | X | X | X | X | X |  | 
 | Presence | X | X |  |  | X |  | X
 | Location | X | X | X | X | X | X | X
 | Address Book | X |  |  |  | X |  | 
Overarching enablers | QoS | X | X | X | X | X |  | 
 | Device/entity mgmt | X | X | X | X | X | X | X
 | Security | X | X | X | X | X | X | X

## Slide 12: Example Use Case: In-Depth Analysis for Facility Management
Facility Management |  | Video surveillance | Utility Metering | Condition monitoring (temp., humidity, …) | Automation (light, air conditioning, etc.) | Alarm system monitoring
Machine-2-machine | Retrieve data | X | X | X | X | X
 | Control devices |  |  |  | X | X
 | Send data |  |  |  | X | X
Human-2-human | A/V Call | X |  |  |  | X
 | A/V conference |  |  |  |  | X
 | Messaging / File transfer |  | X |  |  | 
 | Presence | X |  |  |  | X
 | Location | X | X | X | X | X
 | Address Book | X |  | X |  | 
Overarching enablers | QoS | X |  | X | X | X
 | Device/entity mgmt | X | X |  | X | X
 | Security | X | X | X | X | X

## Slide 13: Smart Cities … making it tangible
Facility Management
E-Health
Utilities
Logistics
Retail and Leisure
eEnergy
Devices, Infrastructure, and Communication Platforms
Facility Management
Facility Management
Video surveillance
Utility Metering
Condition monitoring
Automation
Alarm system monitoring
Devices, Infrastructure, and Communication Platforms
Example sector
Application fields

## Slide 14: Smart Cities … making it tangible
Demos that we have build @ FOKUS
Video surveillance
Utility Metering
Condition monitoring
Automation
Alarm system monitoring
Utility Metering
Condition monitoring
Automation
Facility Management Application fields
http://www.open-mtc.org/_videos/OpenMTC_Demo_video.mp4
Demo video
Communication requirements
Retrieve data
Control devices
Send data
A/V Call
A/V conference
Messaging / File transfer
Presence
Location
Address Book
QoS
Device/entity mgmt
Security

## Slide 15: Definition of a Generic Smart Communication Architecture
Connecting Smart City objects across application domains
Enabling the Internet of Things by using M2M gateways and network middleware to communicate efficiently
Enabling multimedia communication services by integrating Telecoms APIs and platforms.
Enable rapid application development using M2M and H2H network APIs and software development kits (SDK)
Enable cross domain data analytics and fusion to serve the need of Smart Cities

## Slide 16: High-level Architecture Open Communication Server – an open platform for Smart City services

## Slide 17: Elements of the Smart Communications Infrastructure
Sensor
Actuator
Physical Vicinity
(Sensor)
Gateway
Operator Core Network
Mash-Up
Service Platform
Business
Front-end
Operator Networks
Connected
Devices
Services and
Applications
Telecom Network
Light
Temperature
Movement
Gateway to Core-Network
Communication Management
QoS & Charging
Seamless Mobility
Security
M2M resources
M2M session support
Device and connectivity mgmt.
M2M data handling
Application mash-up
Delivery to multimedia warning device

## Slide 18: Future Seamless Communication (FUSECO) Playground
State of the art testbed infrastructure as a cooperation of Berlin’s Next Generation Mobile Network expertise for
  Open IMS for H2H communications
  OpenMTC for M2M communications
  OpenEPC for seamless access
  Various access network technologies
Enabling to prototype application support for
  handover optimization across heterogeneous networks
  support for Always Best Connected (ABC)
  subscriber profile based service personalization
  QoS provisioning and related charging
  controlled access to IMS-based services
  controlled access to Internet/Mobile Clouds

## Slide 19: Use Case: Application-driven QoS for WebRTC
WebRTC communication is enhanced by session-based QoS control.
REST-based API towards PCRF allows setting of QoS policies for temporary bandwidth increase.
Extension of OMA NGSI APIs in FOKUS Cloud Broker for application-driven QoS and network selection.
Mobility manager on Android allows seamless vertical hand-overs.

## Slide 20: Screenshots FOKUS WebRTC to IMS Demo
WebRTC
IMS Client
WebRTC to SIP messaging

## Slide 21: Elasticity for Services Platforms QoS and Network-aware Cross-domain Cloud Brokerage
The FOKUS Elasticity Engine allows for flexible in- and outsourcing of Telco SDPs and services
The choice of Cloud Providers in terms of costs and QoS is dynamically optimized:
    Based on current demand the up-/down-scaling of cloud-resources is dynamically controlled and optimized
    Based on QoS and costs services are dynamically migrated between different cloud providers and cloud platforms
  Thereby QoS-levels are assured and resource consumption ($) is optimized
Cloud
Provider
Internal Cloud
Amazon
RackSpace
FOKUS Elasticity Engine
2G/3G
LTE/LTE-A
WIFI/ WIMAX
Wireless Core Network
LAN/WAN
DSL
Fixed Core Network
$$$
QoS
?
Elasticity
Migration
Notes: Terms:
- Cloud Provider / Cloud Infrastructure: A single provider (usually a company) offering to host services in their very own cloud infrastructure (e.g. Amazon)
- Service Provider: Someone who has implemented a cool new service and would like to make it available by running it in the cloud.
Elastic Cloud Services are great:
- no need for overprovisioning
- start with (and only pay for) one VM
- as soon as demand increases, service will be scaled up
- decreasing demand -> service will be scaled down
- possible to deliver “zero maintenance” solution (just give me the service I’ll cater for the rest)
- already available at some providers albeit with varying features
Added benefit can be obtained by a cross provider solution
- Already some competition among cloud providers, foreseen to surge
- Always choose the best cloud provider for a service instance (where “best” is defined by the service provider)
- makes it possible to service geographically dispersed users from different infrastructures
- Migrate Services across providers when necessary (deteriorating quality, better offer, etc)

## Slide 22: Cloud Control – Elasticity for OpenNebula Clouds
Load Balancer
Users’ requests
Cloud Manager
VM
VM
VM
Measurements
Control operations
Application traffic
Rules Engine
Enactor
Aggregator
VM
VM
VM
Elasticity
Core Network
  Elastic cloud brokering allows optimized resource utilization across multiple sites by dynamic up- & down-scaling
req./s
time
Notes: Elasticity Scenario:
- More requests -> More VMs
- Less requests -> Less VMs

## Slide 23: myMONSTER-RCS Android Communication Client
The software stems
  Extended RCS Stack from Orange Labs for VoLTE
  Compliant to GSMA RCSe 1.2 specification
  Client/Server API allows easy integration with Android native application
Supported RCS/VoLTE key features:
  Enhanced native address book with supported service capabilities and presence info
  Messaging
    File Transfer
    1-1 chat
    Adhoc group chat
    Location
  Rich Call with multimedia content sharing
    Image Sharing
    Video Sharing
    VoIP
Notes: - Enhanced native address book with supported service capabilities and presence info. - Rich messaging with a conversationnal view for chat and file transfer. - Rich call with multimedia content sharing during CS call

## Slide 24: VoLTE Support with many Voice Codecs myMONSTER-RCS
FhI IIS AAC-ELD Codec
  Based on MPEG4 AAC, Low delay
AMR-NB
  Adapts to connection quality by using modes that have different bitrate requirements
GSM
  GSM Full-Rate audio codec (GSM-FR)
GSM_EFR
  GSM Enhanced Full-Rate audio codec
PCMA
  G.711 PCM audio codec with a-law
PCMU
  G.711 PCM audio codec with u-law
FOKUS extensions
  Voice over IP
  Integration with Android RTP API
  Integration of external Codec library for VoIP
  Optimization of video streaming for content sharing
EPC may provide QoS Class Identifier (QCI) for dedicted VoLTE bearer
Android Mobility Manager enables seamless session mobility
Notes: Fraunhofer Institute for Integrated Circuits IIS
The RTP API is available in the android.net.rtp package. Classes include:
RtpStream, the base class of streams that send and receive network packets with media payloads over RTP.
AudioStream, a subclass of RtpStream that carries audio payloads over RTP.
AudioGroup, a local audio hub for managing and mixing the device speaker, microphone, and AudioStream.
AudioCodec, which holds a collection of codecs that you define for an AudioStream.
To support audio conferencing and similar usages, an application instantiates two classes as endpoints for the stream:
AudioStream specifies a remote endpoint and consists of network mapping and a configured AudioCodec.
AudioGroup represents the local endpoint for one or more AudioStreams. The AudioGroup mixes all theAudioStreams and optionally interacts with the device speaker and the microphone at the same time.

## Slide 25: Success Story VoIP / IP Multimedia Subsystem Providing open source software and toolkits
Early prototyping of Session Initiation Protocol (SIP) server resulted in successful open source project SIP Express Router
  Licenses have been sold to Tekelec through spinning-off iptel.org GmbH
Continuation of development as open source IP Multimedia Subsystem helped FOKUS to gain world-wide knowledge in the telecommunications industry and network operators.
Development of service and development tool kits as non open source solutions building on top of the open source software provided the basis for licenses and joined RnD projects with operators as NTT, Telkom Indonesia, Vodafone, Deutsche Telekom, STC.
Europe
Asia
Americas
Statistics for Open Source project OpenIMS access
FOKUS cooperations with industry partners worldwide

## Slide 26: The FOKUS OpenMTC Platform
Based on the success of the Open IMS Core and OpenEPC Fraunhofer FOKUS has developed a NON-OPEN SOURCE Machine Type Communication platform, enabling academia and industry to:
  integrate various machine devices with operator networks
  integrate various application platforms and services
into a single local testbed, thus lowering own development costs
OpenMTC is an intermediary layer between multiple service platforms, the operator network, and devices
This platform can be used to perform R&D in the
fields of machine type communication
OpenMTC implemented features are aligned with ETSI M2M specifications:
  Adaptable to different M2M scenarios (e.g. automotive)
  Extensible to specific research needs
  Configurable
  Performant
  see wwww.open-MTC.org

## Slide 27: OpenMTC Architecture – Release 1
OpenMTC consists of the two main components
  Network Service Capability Layer (NSCL)
  Gateway Service Capability Layer (GSCL)
Both SCLs contain several modules
  e.g. NGC: Network generic communication, GSEC: Gateway security, etc.
  Some of them are optional
OpenMTC allows interworking with
  OpenEPC (Evolved Packet Core)
  OpenIMS (IP Multimedia Subsystem)
  FOKUS Service Broker
OpenMTC supports:
  Various sensors and actuators (e.g. ZigBee, FS20 devices)
  Multiple Access networks (e.g. fixed, mobile, xDSL, 3G, etc.)
  Various Applications (e.g. Smart Cities, Smart Home, etc.)

## Slide 28: OpenMTC SDK - Standard interface toward the OpenMTC core
Providing developers with standard interface toward the OpenMTC that consists of different service capabilities.
Enabling the OpenMTC SDK within the FOKUS Broker.
  Fast way to combine M2M information with telecommunication or Internet services.
  Allows the creation of new value added services.

## Slide 29: Success Story IP Connectivity / Evolved Packet System Providing open test-bed software and toolkits
First-time implementation of the latest Next Generation Fixed and Mobile Network architectures and concepts
  Working with major NEPs towards validation of new concepts for NGN-to-Future-Internet evolutions
  Providing small NEPs with a comprehensive prototyping environment
  Establishing test-beds and performing field-trials with major operators towards accelerating the adoption of new technologies
  Enabling the academia with access to the state-of-the-art open prototypes
OpenEPC
  Complements the Open Source IMS Core in providing a comprehensive Voice-over-LTE experimentation
  Provides IP connectivity for Heterogeneous Radio Access Networks
Currently powering world-wide laboratories of 4 major telco operators, 5 universities, 3 research organizations and many commercial companies

## Slide 30: What is FOKUS OpenEPC Platform?
Future massive broadband communications will be realized through multi-access support (LTE, 3G, 2G, WiFi, fixed networks …) and multi-application domains (OTT, IMS, P2P, M2M, Cloud, …)
Fraunhofer FOKUS is developing the NON-OPEN SOURCE OpenEPC toolkit, enabling to:
  integrate various network technologies and
  integrate various application platforms
  into a single local testbed, thus lowering own development costs
This platform can be used to perform R&D in the fields of
  QoS, Charging, Mobility, Security, Management, Monitoring
OpenEPC represents a software implementation of the 3GPP
EPC standard addressing academia and industry R&D:
  Based on 3GPP standards
  Configurable to different deployments
  Customizable to the various testbed requirements
  Extensible to specific research needs
  Reliable & highly performant
More information: www.OpenEPC.net

## Slide 31: OpenEPC: Features, Functionality, and Components
Core Network Mobility Management
Core Network Support for 3GPP Accesses
  LTE Access Network Integration
  HSPA/UMTS Access Network Integration
  EDGE/GPRS Access Network Integration
Non-3GPP Access Networks AAA
Policy and Charging Control
Accounting and Charging
Subscriber Management & Provisioning
User Plane Realization
Client Mobility Management
Distribution Features
Interconnection with Access Networks & Devices
Interconnection with Applications and Services

## Slide 32: OpenEPC+OpenIMS: Just add Radio, Devices and Applications

## Slide 33: Working with Off-the-Shelf Devices

## Slide 34
Preview
Nov. 2009
Rel. 1
April 2010
Rel. 2
Feb 2011
Rel. 3
Jan 2012
Rel. 4
Nov 2012
Rel. 5/6
…
First demo of the OpenEPC at the 5th IMS Workshop
Core Network Mobility
Client Mobility
Policy and Charging Control
Subscription Management
Mobile Device support
Extended Mobility
(GTP, MME etc.)
Extended AAA
More Access Networks Integration
Support for specific applications
Integration of 3GPP
Offline Charging
Non-3GPP AAA
Extended UE function
Dynamic node selection
Full NAS, GTP stacks
S1AP with APER, X2AP
LTE RAN integration
2G and 3G RAN integration
Android Mobile Devices Support
Multiple APN Support
Radio conditions based handover
Traffic Shaping for QoS
OpenFlow and SDN-EPC
VoLTE with SRVCC
Network Functions Virtualization
UE/eNodeB-emulation-with-WiFi
Self Organized Networks Features
…

## Slide 35: Network Functions Virtualization (NFV)
Network Functions Virtualization (NFV) is a novel paradigm that presumes that the network functions:
  Are implemented only as software (programs)
  Can run on top of common servers
NFV implies that network functions:
  Can be moved as required
  Do not require special equipment
© NFV White Paper presented at “SDN and OpenFlow World Congress”, Darmstadt Oct 22-24, 2012

## Slide 36: What’s next: Network Functions Virtualization (NFV)
Network Functions Virtualization (NFV) is a novel paradigm that presumes that the network functions:
  Are implemented only as software (programs)
  Can run on top of common servers
Research directions:
  Are the cloud infrastructures ready to deploy NFV (delay, capacity, parallelism)
  Virtualized infrastructures management (networking, elasticity, failover)
  Defining the next core network architecture

## Slide 37: What’s next: Mobile Telco Architecture Evolution Path  SDN
GGSN
SGSN
RNC
NodeB
PGW
SGW
eNB
MME
OpenFlow Control Plane
Data Plane
3GPP Control Plane
UMTS
SAE/EPS r12
Mobile Telco Architecture Evolution Path
GGSN
RNC
NodeB
HSPA r7
SGSN
GGSN
NodeB
HSPA r8
SGSN
GGSN
SGSN
BSC
NodeB
UMTS
BTS
eNB
MME
PGW
-C
SGW
-C
SAE/EPS+OF
PGW
-D
SGW
-D

## Slide 38: Step 1: Virtualize the Control Plane
Run in the data center software components for : PCRF, HSS, AAA, MME, ANDSF, DPI, OCS, OFCS, ….

## Slide 39: Step 2: Split the User Plane and Use SDN switches
EPC Control, Mobility and all signaling can be virtualized
But the User Data Plane stays in the infrastructure for maximum performance

## Slide 40: What’s next: Elastic and Flexible Network Design - Example EPS
Elastic network design aligned on real-time network load situations
Enablement and disablement of redundant access- and core-network elements
Optimized energy consumption of the access- and core-network
Network Resources as a Service (NRaaS) and on demand

## Slide 41
Commercial FOKUS NGN/IMS/EPC/SOA Testbed Deployments around the world

## Slide 42: EU Mobile Cloud Networking Project makes use of OpenEPC for EPCaaS Prototyping
FP7 Intergated Project started in November 2012 for 36 month targeting for bringing cloud computing features to mobile operator core networks (EPCaaS):
  Virtualization of components
  Software defined networks
  Elasticity
  Total distribution
  Infrastructure sharing
  Redefining roaming
OpenEPC is used as the basis platform for mobile core network experimentation
Mobile Cloud
Networking
For more: http://mobile-cloud-networking.eu

## Slide 43: 4th FOKUS „Future Seamless Communication“ Forum (FFF) Berlin, Germany, November 28-29, 2013
Theme: „Smart Communications Platforms for Seamless Smart City Applications – Fixed and Mobile Next Generation Networks Evolution towards virtualized network control and service platforms and Seamless Cloud-based H2H and M2M Applications“
FUSECO FORUM is the successor of the famous FOKUS IMS Workshop series (2004-09)
  FFF 2010 attracted 150 experts from 21 nations
  FFF 2011 was attended by around 200 experts from 30 nations
  FFF 2012 was attended again by around 200 experts from 30 nations
See www.fuseco-forum.org

## Slide 44: Contact
Thomas Magedanz
Prof. Dr.
Head of Competence Center
Next Generation Network Infrastructures
Fraunhofer Institute for Open Communication Systems
Kaiserin-Augusta-Allee 31 | 10589 Berlin | Germany
Phone +49 30 3463 - 7229 | Fax -8000
thomas.magedanz@fokus.fraunhofer.de
www.fokus.fraunhofer.de